Max. Source file length: ~2Gb
Max. database line number: ? 32000

1. CSV content:

1) Encoding – according to "CodePage" setting in the EscPosParser2.exe.config file (default "866")
2) Column divider - according to "CSVdelimiter" setting in the EscPosParser2.exe.config file (default ";")

2. Command data base columns:
1) Command (HEX) – command string [HEX string]
2) Command description – description of command, parameter or predefined parameter
3) Command parameter size (DEC) – length of the parameter [byte]
4) Command parameter type – parameter type. Defines how to show/decode data.
5) Command parameter value (dec) – predefined parameter values if any.
6) Reply parameter size (DEC) – length of the parameter [byte]
7) Reply parameter type – parameter type. Defines how to show/decode data.
8) Reply parameter value (dec) – predefined parameter values if any.
9) Reply description – description of command, parameter or predefined parameter
10) Comments – always ignored. Needed only for correct CSV processing.
All other columns ignored.

3. Possible parameter types:
1) string – Length: until byte shown in predefined value; displayed if printable.
2) number – int number displayed, last significant byte.
3) number_invert – int number displayed, first significant byte.
4) money – float number displayed, last significant byte.
5) money_invert – float number displayed, first significant byte.
6) data - Length: until byte shown in predefined value; displayed if printable.
7) bitfield - Length: until byte shown in predefined value; A numerical value displayed.

6. Command data base structure:
Each command or parameter must have it’s 1st line clear except “Description”.
Each parameter may have several predefined values to define proper description on the lines	next to parameter definition.
 Description for predefined value is added to description of the parameter in the program	GUI.
Each parameter must be followed by a parameter type definition.
“bitfield” parameter is followed by 8 lines describing each bit
Parameter size can be a number or "?" - then it's size assumed as "till the end of the frame" minus all following parameter sizes.